## Slide 1: 计算机体系结构
周学海
xhzhou@ustc.edu.cn
0551-63601556, 63492271
中国科学技术大学

## Slide 2: 第6章 Data-Level Parallelism in Vector, SIMD, and GPU Architectures
SIMD的变体
向量体系结构
GPU

## Slide 3: review: Multithreading
Time (processor cycle)
Superscalar
Fine-Grained
Coarse-Grained
Multiprocessing
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
Idle slot

## Slide 4: 传统指令级并行技术的问题
挖掘ILP的传统方法的主要缺陷:
提高流水线的时钟频率: 提高时钟频率，有时导致CPI随着增加 (branches, other hazards)
指令预取和译码: 有时在每个时钟周期很难预取和译码多条指令
提高Cache命中率 : 在有些计算量较大的应用中（科学计算）需要大量的数据，其局部性较差，有些程序处理的是连续的媒体流(multimedia),其局部性也较差。

## Slide 5: Introduction
SIMD 结构可有效地挖掘数据级并行:
  基于矩阵运算的科学计算
  图像和声音处理
SIMD比MIMD更节能
  针对每组数据操作仅需要取指一次
  SIMD对PMD( personal mobile devices)更具吸引力
SIMD 允许程序员继续以串行模式思维

## Slide 6: SIMD Parallelism
向量体系结构
SIMD 扩展
Graphics Processor Units (GPUs)
For x86 processors:
  每年增加2cores/chip
  SIMD 宽度每4年翻一番
  SIMD潜在加速比是MIMD的2倍

## Slide 7: Supercomputers
Definition of a supercomputer:
  对于给定任务而言世界上最快的机器
  将计算密集型转化为I/O密集型的设备
  任何造价超过3千万美元的机器
由Seymour Cray设计的机器
CDC6600 (Cray, 1964) 被认为是第一台超级计算机`

## Slide 8: CDC 6600 Seymour Cray, 1963
A fast pipelined machine with 60-bit words
  128 Kword main memory capacity, 32 banks
Ten functional units (parallel, unpipelined)
  Floating Point: adder, 2 multipliers, divider
  Integer: adder, 2 incrementers, ...
Hardwired control (no microcoding)
Scoreboard for dynamic scheduling of instructions
Ten Peripheral Processors for Input/Output
  a fast multi-threaded 12-bit integer ALU
Very fast clock, 10 MHz (FP add in 4 clocks)
>400,000 transistors, 750 sq. ft., 5 tons, 150 kW, novel freon-based technology for cooling
Fastest machine in world for 5 years (until 7600)
  over 100 sold ($7-10M each)

## Slide 9: IBM Memo on CDC6600
Thomas Watson Jr., IBM CEO, August 1963:
  “Last week, Control Data ... announced the 6600 system. I understand that in the laboratory developing the system there are only 34 people including the janitor. Of these, 14 are engineers and 4 are programmers... Contrasting this modest effort with our vast development activities, I fail to understand why we have lost our industry leadership position by letting someone else offer the world's most powerful computer.”
To which Cray replied: “It seems like Mr. Watson has answered his own question.”

## Slide 10: Supercomputer Applications
典型应用领域
  军事研究领域（核武器研制、密码学）
  科学研究
  天气预报
  石油勘探
  工业设计 (car crash simulation)
  生物信息学
  密码学
均涉及大量的数据集处理
70-80年代Supercomputer = Vector Machine

## Slide 11: Alternative Model:Vector Processing
向量处理机具有更高层次的操作，一条向量指令可以处理N个或N对操作数（处理对象是向量）
+
r1
r2
r3
add r3, r1, r2
SCALAR
(1 operation)
v1
v2
v3
+
vector
length
add.vv v3, v1, v2
VECTOR
(N operations)
Notes: 25

## Slide 12: 向量处理机的基本特性
基本思想：两个向量的对应分量进行运算，产生一个结果向量。
简单的一条向量指令包含了多个操作=> fewer instruction fetches
每一结果独立于前面的结果
  长流水线，编译器保证操作间没有相关性
  硬件仅需检测两条向量指令间的相关性
  较高的时钟频率
向量指令以已知的模式访问存储器
  可有效发挥多体交叉存储器的优势
  可通过重叠减少存储器操作的延时 ­ 64 elements
  不需要数据Cache! (仅使用指令cache)
在流水线控制中减少了控制相关

## Slide 13: 向量处理机的基本结构
memory-memory vector processors: 所有的向量操作是存储器到存储器
vector-register processors: 除了load 和store操作外，所有的操作是向量寄存器与向量寄存器间的操作
  向量机的Load/Store结构
  1980年以后的所有的向量处理机都是这种结构: Cray, Convex, Fujitsu, Hitachi, NEC
  我们也主要针对这种结构

## Slide 14: 向量处理机的基本组成单元
Vector Register: 固定长度的一块区域，存放单个向量
  至少2个读端口和一个写端口
  典型的有8-32 向量寄存器，每个寄存器存放64到128个64位的元素
Vector Functional Units (FUs): 全流水化的，每一个clock启动一个新的操作
  一般4到8个FUs: FP add, FP mult, FP reciprocal (1/X), integer add, logical, shift; 可能有些重复设置的部件
Vector Load-Store Units (LSUs): 全流水化地load 或store一个向量，可能会配置多个LSU部件
Scalar registers: 存放单个元素用于标量处理或存储地址
用交叉开关连接(Cross-bar to connect) FUs , LSUs, registers

## Slide 16: Vector Supercomputers
Cray-1的变体（1976）:
Scalar Unit：Load/Store Architecture
Vector Extension
  Vector Registers
  Vector Instructions
Implementation
  硬布线逻辑控制
  高效流水化的功能部件
  多体交叉存储系统
  无Data Cache
  不支持 Virtual Memory

## Slide 17: Vector Instruction Set Advantages
格式紧凑
  一条指令包含N个操作
表达能力强, 一条指令能告诉硬件:
  N个操作之间无相关性
  使用同样的功能部件
  访问不相交的寄存器
  与前面的操作以相同模式访问寄存器
  访问存储器中的连续块 (unit-stride load/store)
  以已知的模式访问存储器 (strided load/store)
可扩展性好
  可以在多个并行的流水线上运行同样的代码 (lanes)

## Slide 18: Vector Arithmetic Execution
使用较深的流水线(=> fast clock) 执行向量元素的操作
由于向量元素相互独立，简化了的深度流水线的控制 (=> no hazards!)
V1
V2
V3
V3 <- v1 * v2
Six stage multiply pipeline

## Slide 19: Vector Instruction Execution
ADDV C,A,B
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
使用一条流水化的功能部件执行
C[4]
C[8]
C[0]
A[12]
B[12]
A[16]
B[16]
A[20]
B[20]
A[24]
B[24]
C[5]
C[9]
C[1]
A[13]
B[13]
A[17]
B[17]
A[21]
B[21]
A[25]
B[25]
C[6]
C[10]
C[2]
A[14]
B[14]
A[18]
B[18]
A[22]
B[22]
A[26]
B[26]
C[7]
C[11]
C[3]
A[15]
B[15]
A[19]
B[19]
A[23]
B[23]
A[27]
B[27]
使用4条流水化的功能部件执行

## Slide 20: Interleaved Vector Memory System
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
+
Base
Stride
Vector Registers
Memory Banks
Address Generator
Cray-1, 16 banks, 4 cycle bank busy time, 12 cycle latency
  Bank busy time: Time before bank ready to accept next request

## Slide 21: Vector Unit Structure
Lane
Functional Unit
Vector
Registers
Memory Subsystem
Elements 0, 4, 8, …
Elements 1, 5, 9, …
Elements 2, 6, 10, …
Elements 3, 7, 11, …

## Slide 22: T0 Vector Microprocessor (UCB/ICSI, 1995)
Lane
Vector register elements striped over lanes
[0]
[8]
[16]
[24]
[1]
[9]
[17]
[25]
[2]
[10]
[18]
[26]
[3]
[11]
[19]
[27]
[4]
[12]
[20]
[28]
[5]
[13]
[21]
[29]
[6]
[14]
[22]
[30]
[7]
[15]
[23]
[31]

## Slide 23: Vector Instruction Parallelism
多条向量指令可重叠执行
  例如：每个向量 32 个元素，8 lanes（车道）
load
load
mul
mul
add
add
Load Unit
Multiply Unit
Add Unit
time
Instruction issue
Complete 24 operations/cycle while issuing 1 short instruction/cycle

## Slide 24: “DLXV” Vector Instructions
Instr. Operands Operation Comment
ADDV V1,V2,V3 V1=V2+V3 vector + vector
ADDSV V1,F0,V2 V1=F0+V2 scalar + vector
MULTV V1,V2,V3 V1=V2xV3 vector x vector
MULSV V1,F0,V2 V1=F0xV2 scalar x vector
LV V1,R1 V1=M[R1..R1+63] load, stride=1
LVWS V1,R1,R2 V1=M[R1..R1+63*R2] load, stride=R2
LVI V1,R1,V2 V1=M[R1+V2i,i=0..63] indir.("gather")
CeqV VM,V1,V2 VMASKi = (V1i=V2i)? comp. setmask
MOV VLR,R1 Vec. Len. Reg. = R1 set vector length
MOV VM,R1 Vec. Mask = R1 set vector mask

## Slide 25: Vector Execution Time
Time = f(vector length, data dependencies, struct. hazards)
Initiation rate: 功能部件消耗向量元素的速率
Convoy: 可在同一时钟周期开始执行的指令集合 (no structural or data hazards)
Chime: 执行一个convoy所花费的大致时间（approx. time）
m convoys take m chimes; 如果每个向量长度为n, 那么m个convoys 所花费的时间是m个chimes，每个chime所花费的时间是n个clocks，该程序所花费的总时间大约为m x n clock cycles (ignores overhead; good approximization for long vectors)
4 convoys, 1 lane, VL=64
=> 4 x 64 = 256 clocks
(or 4 clocks per result)
1: LV V1,Rx ;load vector X
2: MULV V2,F0,V1 ;vector-scalar mult.
LV V3,Ry ;load vector Y
3: ADDV V4,V2,V3 ;add
4: SV Ry,V4 ;store the result

## Slide 26: Vector Startup
向量启动时间由两部分构成
  功能部件延时：一个操作通过功能部件的时间
  截止时间或回复时间（dead time or recovery time ）：运行下一条向量指令的间隔时间
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
Functional Unit Latency
Dead Time
First Vector Instruction
Second Vector Instruction
Dead Time

## Slide 27: Dead Time and Short Vectors
Cray C90, Two lanes
4 cycle dead time
Maximum efficiency 94% with 128 element vectors
4 cycles dead time
T0, Eight lanes
No dead time
100% efficiency with 8 element vectors
No dead time
64 cycles active

## Slide 28: DLXV Start-up Time
Start-up time: FU 部件流水线的深度
Operation Start-up penalty (from CRAY-1)
Vector load/store 12
Vector multiply 7
Vector add 6
  Assume convoys don't overlap; vector length = n
Convoy Start 1st result last result
1. LV 0 12 11+n (12+n-1)
2. MULV, LV 12+n 12+n+7 18+2n Multiply startup
12+n 12+n+12 23+2n Load start-up
3. ADDV 24+2n 24+2n+6 29+3n Wait convoy 2
4. SV 30+3n 30+3n+12 41+4n Wait convoy 3

## Slide 29: Vector Length
当向量的长度不是64时（假设向量寄存器的长度是64）怎么办？
vector-length register (VLR) 控制特定向量操作的长度, 包括向量的load/store. (当然一次操作的向量的长度不能 > 向量寄存器的长度) 例如：
do 10 i = 1, n
10 Y(i) = a * X(i) + Y(i)
n的值只有在运行时才能知道 n > Max. Vector Length (MVL)怎么办？

## Slide 30: Strip Mining（分段开采）
假设Vector Length > Max. Vector Length (MVL)?
Strip mining: 产生新的代码，使得每个向量操作的元素数  MVL
第一次循环做最小片(n mod MVL), 以后按VL = MVL操作
low = 1 VL = (n mod MVL) /*find the odd size piece*/ do 1 j = 0, (n / MVL) /*outer loop*/
do 10 i = low, low+VL-1 /*runs for length VL*/ Y(i) = a*X(i) + Y(i) /*main operation*/ 10 continue low = low+VL /*start of next vector*/ VL = MVL /*reset the length to max*/ 1 continue

## Slide 31: Strip Mining的向量执行时间计算
试计算A=B×s，其中A,B为长度为200的向量（每个向量元素占8个字节），s是一个标量。向量寄存器长度为64。各功能部件的启动时间如前所述，求总的执行时间，(Tloop = 15)

## Slide 32
ADDI R2,R0,#1600 ;total # bytes in vector
ADD R2,R2,Ra ;address of the end of A vector
ADDI R1,R0,#8 ;loads length of 1st segment
MOVI2S VLR,R1 ;load vector length in VLR
ADDI R1,R0,#64 ;length in bytes of 1st segment
ADDI R3,R0,#64 ;vector length of other segments
Loop: LV V1,Rb ;load B
MULSV V2,V1,Fs ;vector * scalar
SV Ra,V2 ;store A
ADD Ra,Ra,R1 ;address of next segment of A
ADD Rb,Rb,R1 ;address of next segment of B
ADDI R1,R0,#512 ;load byte offset next segment
MOVI2S VLR,R3 ;set length to 64 elements
SUB R4,R2,Ra ;at the end of A?
BNEZ R4,Loop ;if not, go back

## Slide 33
Tstart = 12 + 7 + 12 = 31
T200 = 660+4*31 = 784
每一元素的执行时间 = 784/200 = 3.9

## Slide 35: Common Vector Metrics
R: 当向量长度为无穷大时的向量流水线的最大性能。常在评价峰值性能时使用，单位为MFLOPS
  实际问题是向量长度不会无穷大，start-up的开销还是比较大的
  Rn 表示向量长度为n时的向量流水线的性能
N1/2: 达到R 一半的值所需的向量长度，是评价向量流水线start-up 时间对性能的影响。
NV: 向量流水线方式的工作速度优于标量串行方式工作时所需的向量长度临界值。
  该参数既衡量建立时间，也衡量标量、向量速度比对性能的影响

## Slide 36: Vector Stride
假设处理顺序相邻的元素在存储器中不是顺序存储。例如
do 10 i = 1,100
do 10 j = 1,100
A(i,j) = 0.0
do 10 k = 1,100
10 A(i,j) = A(i,j)+B(i,k)*C(k,j)
B 或 C 的两次访问不会相邻 (相隔800 bytes)
stride: 向量中相邻元素间的距离 => LVWS (load vector with stride) instruction
Strides => 会导致体冲突 (e.g., stride = 32 and 16 banks)

## Slide 37: Memory operations
32
Load/store 操作成组地在寄存器和存储器之间移动数据
三类寻址方式
  Unit stride (单步长)
    Fastest
  Non-unit (constant) stride (常数步长)
  Indexed (gather-scatter) (间接寻址)
    等价于寄存器间接寻址方式
    对稀疏矩阵有效
    用于向量化操作的指令增多
Notes: 32

## Slide 38: DAXPY (Y = a * X + Y)
LD F0,a
ADDI R4,Rx,#512 ;last address to load
loop: LD F2, 0(Rx) ;load X(i)
MULTD F2,F0,F2 ;a*X(i)
LD F4, 0(Ry) ;load Y(i)
ADDD F4,F2, F4 ;a*X(i) + Y(i)
SD F4 ,0(Ry) ;store into Y(i)
ADDI Rx,Rx,#8 ;increment index to X
ADDI Ry,Ry,#8 ;increment index to Y
SUB R20,R4,Rx ;compute bound
BNZ R20,loop ;check if done
LD F0,a ;load scalar a
LV V1,Rx ;load vector X
MULTS V2,F0,V1 ;vector-scalar mult.
LV V3,Ry ;load vector Y
ADDV V4,V2,V3 ;add
SV Ry,V4 ;store the result
Assuming vectors X, Y are length 64
Scalar vs. Vector
578 (2+9*64) vs. 321 (1+5*64) ops (1.8X)
578 (2+9*64) vs. 6 instructions (96X)
64 operation vectors + no loop overhead
also 64X fewer pipeline hazards

## Slide 39: Example Vector Machines
Machine Year Clock Regs Elements FUs LSUs
Cray 1 1976 80 MHz 8 64 6 1
Cray XMP 1983 120 MHz 8 64 8 2 L, 1 S
Cray YMP 1988 166 MHz 8 64 8 2 L, 1 S
Cray C-90 1991 240 MHz 8 128 8 4
Cray T-90 1996 455 MHz 8 128 8 4
Conv. C-1 1984 10 MHz 8 128 4 1
Conv. C-4 1994 133 MHz 16 128 3 1
Fuj. VP200 1982 133 MHz 8-256 32-1024 3 2
Fuj. VP300 1996 100 MHz 8-256 32-1024 3 2
NEC SX/2 1984 160 MHz 8+8K 256+var 16 8
NEC SX/3 1995 400 MHz 8+8K 256+var 16 8
Notes: Cray 1; fastest scalar computer + 1st commercially successful vector computer, offered another 10X
6600 1st scoreboard
Cray XMP: 3 LSUs, Multiprocessor 4 way (not by Cray)
=> YMP, C-90, T-90; 2X processors, 1.5X clock
Cray 2 went to DRAM to get more memory, not so great
Like parallel teams as Intel (486, PPro, Pentium, next one)
Japan
Fujitsu, vary number of registers elements (8x1024 or 32x256)
NEC, 8x256 + 8K of varying elements

## Slide 40: Vector Linpack Performance (MFLOPS)
Machine Year Clock 100x100 1kx1k Peak(Procs)
Cray 1 1976 80 MHz 12 110 160(1)
Cray XMP 1983 120 MHz 121 218 940(4)
Cray YMP 1988 166 MHz 150 307 2,667(8)
Cray C-90 1991 240 MHz 387 902 15,238(16)
Cray T-90 1996 455 MHz 705 1603 57,600(32)
Conv. C-1 1984 10 MHz 3 -- 20(1)
Conv. C-4 1994 135 MHz 160 2531 3240(4)
Fuj. VP200 1982 133 MHz 18 422 533(1)
NEC SX/2 1984 166 MHz 43 885 1300(1)
NEC SX/3 1995 400 MHz 368 2757 25,600(4)
Matrix Inverse (gaussian elimination)
Notes: 6X in 20 years; 32X in 20 years; Peak is 360X speedup
Weighed tons

## Slide 41: Vector Opt#1: Vector Chaining
寄存器定向路径的向量机版本
首次在Cray-1上使用
Memory
V1
Load Unit
Mult.
V2
V3
Chain
Add
V4
V5
Chain
LV v1
MULV v3,v1,v2
ADDV v5, v3, v4

## Slide 42: Vector Chaining Advantage
采用链接技术，前一条指令的第一个结果出来后，就可以启动下一条相关指令的执行
Load
Mul
Add
Load
Mul
Add
Time
不采用链接技术，必须处理完前一条指令的最后一个元素，才能启动下一条相关的指令

## Slide 43: Vector Opt #2: Conditional Execution
Suppose:
do 100 i = 1, 64
if (A(i) .ne. 0) then
A(i) = A(i) – B(i)
endif
100 continue
vector-mask control 使用长度为MVL的布尔向量控制向量指令的执行
当vector-mask register 使能时，向量指令操作仅对 vector-mask register中 对应位为1的分量起作用

## Slide 44: Masked Vector Instructions
C[4]
C[5]
C[1]
Write data port
A[7]
B[7]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
M[7]=1
Density-Time Implementation
  scan mask vector and only execute elements with non-zero masks
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
Write data port
Write Enable
A[7]
B[7]
M[7]=1
Simple Implementation
  execute all N operations, turn off result writeback according to mask

## Slide 45
LV V1,Ra ; load vector A into V1
LV V2,Rb ; load vector B
L.D F0,#0 ; load FP zero into F0
SNEVS.D V1,F0 ;sets VM(i) to 1 if V1(i)!=F0
SUBV.D V1,V1,V2 ;subtract under vector mask
CVM ;set the vector mask to all 1s
SV Ra,V1 ;store the result in A
使用vector-mask寄存器的缺陷
  简单实现时，条件不满足时向量指令仍然需要花费时间
  有些向量处理器带条件的向量执行仅控制向目标寄存器的写操作，可能会有除法错。

## Slide 46: Vector Opt #3: Sparse Matrices
Suppose:
do 100 i = 1,n
100 A(K(i)) = A(K(i)) + C(M(i))
gather (LVI) operation 使用index vector 中给出的偏移再加基址来读取 => a nonsparse vector in a vector register
这些元素以密集的方式操作完成后，再使用同样的index vector存储到稀疏矩阵的对应位置
这些操作编译时可能无法完成。主要原因：编译器无法预知Ki以及是否有数据相关
使用CVI 设置步长（ index 0, 1xm, 2xm, ..., 63xm）
Notes: CVI gets used under mask

## Slide 47: Sparse Matrix Example
Cache (1993) vs. Vector (1988)
IBM RS6000 Cray YMP
Clock 72 MHz 167 MHz
Cache 256 KB 0.25 KB
Linpack 140 MFLOPS 160 (1.1)
Sparse Matrix 17 MFLOPS 125 (7.3) (Cholesky Blocked )
Cache: 1 address per cache block (32B to 64B)
Vector: 1 address per element (4B)

## Slide 48: Automatic Code Vectorization
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
向量化是指在编译期间对操作重定序 需要进行大量的循环相关分析
Vector Instruction
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Vectorized Code
Time

## Slide 49: A Modern Vector Super: NEC SX-9 (2008)
65nm CMOS technology
Vector unit (3.2 GHz)
  8 foreground VRegs + 64 background VRegs (256x64-bit elements/VReg)
  64-bit functional units: 2 multiply, 2 add, 1 divide/sqrt, 1 logical, 1 mask unit
  8 lanes (32+ FLOPS/cycle, 100+ GFLOPS peak per CPU)
  1 load or store unit (8 x 8-byte accesses/cycle)
Scalar unit (1.6 GHz)
  4-way superscalar with out-of-order and speculative execution
  64KB I-cache and 64KB data cache
Memory system provides 256GB/s DRAM bandwidth per CPU
Up to 16 CPUs and up to 1TB DRAM form shared-memory node
  total of 4TB/s bandwidth to shared DRAM memory
Up to 512 nodes connected via 128GB/s network links (message passing between nodes)
Notes: Picture from NEC article “A hardware overview of SX-6 and SX-7 supercomputer”

## Slide 50: Vector Memory-Memory versus Vector Register Machines
存储器-存储器型向量机所有指令操作的操作数来源于存储器
第一台向量机 CDC Star-100 (‘73) and TI ASC (‘71), 是存储器-存储器型机器were memory-memory machines
Cray-1 (’76) 是第一台寄存器型向量机
for (i=0; i<N; i++)
{
C[i] = A[i] + B[i];
D[i] = A[i] - B[i];
}
Example Source Code
ADDV C, A, B
SUBV D, A, B
Vector Memory-Memory Code
LV V1, A
LV V2, B
ADDV V3, V1, V2
SV V3, C
SUBV V4, V1, V2
SV V4, D
Vector Register Code

## Slide 51: Vector Memory-Memory vs. Vector Register Machines
存储器-存储器型向量机 (VMMA) 需要更高的存储器带宽
  All operands must be read in and out of memory
VMMAs结构使得多个向量操作重叠执行更困难
  Must check dependencies on memory addresses
VMMAs 启动时间更长
  CDC Star-100 在向量元素小于100时，标量代码的性能高于向量化代码
  For Cray-1, vector/scalar 均衡点在2个元素
CDC Cray-1后续的机器 (Cyber-205, ETA-10) 都是寄存器型向量机

## Slide 52: Multimedia Extensions (aka SIMD extensions)
在已有的ISA中添加一些向量长度很短的向量操作指令
将已有的 64-bit 寄存器拆分为 2x32b or 4x16b or 8x8b
  1957年，Lincoln Labs TX-2 将36bit datapath 拆分为2x18b or 4x9b
  新的设计具有较宽的寄存器
    128b for PowerPC Altivec, Intel SSE2/3/4
    256b for Intel AVX
单条指令可实现寄存器中所有向量元素的操作
16b
16b
16b
16b
32b
32b
64b
8b
8b
8b
8b
8b
8b
8b
8b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
+
+
+
+
4x16b adds

## Slide 53: Multimedia Extensions versus Vectors
受限的指令集:
  无向量长度控制
  Load/store操作无 常数步长寻址和 scatter/gather操作
  loads 操作必须64/128-bit 边界对齐
受限的向量寄存器长度:
  需要超标量发射以保持multiply/add/load 部件忙
  通过循环展开隐藏延迟增加了寄存器读写压力
在微处理器设计中向全向量化发展
  更好地支持非对齐存储器访问
  支持双精度浮点数操作 (64-bit floating-point)
  Intel AVX spec (announced April 2008), 256b vector registers (expandable up to 1024b)

## Slide 54: Types of Parallelism
Instruction-Level Parallelism (ILP)
  Execute independent instructions from one instruction stream in parallel (pipelining, superscalar, VLIW)
Thread-Level Parallelism (TLP)
  Execute independent instruction streams in parallel (multithreading, multiple cores)
Data-Level Parallelism (DLP)
  Execute multiple operations of the same type in parallel (vector/SIMD execution)
Which is easiest to program?
Which is most flexible form of parallelism?
  i.e., can be used in more situations
Which is most efficient?
  i.e., greatest tasks/second/area, lowest energy/task

## Slide 55: Resurgence of DLP
应用需求和技术约束推动着体系结构的发展和选择
图形、机器视觉、语音识别、机器学习等新的应用均需要大量的数值计算，其算法通常具有数据并行
SIMD-based 结构 (vector-SIMD, subword-SIMD, SIMT/GPUs) 是执行这些算法的最有效途径

## Slide 56: DLP important for conventional CPUs too
Prediction for x86 processors, from Hennessy & Patterson, 5th edition
  Note: Educated guess, not Intel product plans!
TLP: 2+ cores / 2 years
DLP: 2x width / 4 years
DLP will account for more mainstream parallelism growth than TLP in next decade.
  SIMD –single-instruction multiple-data (DLP)
  MIMD- multiple-instruction multiple-data (TLP)

## Slide 57: Graphics Processing Units (GPUs)
原来的GPU是指带有高性能浮点运算部件、可高效生成3D图形的具有固定功能的专用设备 (mid-late 1990s)
  让PC机具有类似工作站的图形功能
  用户可以配置图形处理流水线，但不是真正的对其编程
随着时间的推移，GPU加入了越来越多的可编程性 (2001-2005)
  例如新的语言 Cg可用来编写一些小的程序处理图形的顶点或像素，是Windows DirectX的变体
  大规模并行（针对每帧上百万顶点或像素）但非常受限于编程模型
有些用户注意到通过将输入和输出数据映射为图像，并对顶点或像素渲染计算 可进行通用计算
  因为不得不使用图形流水线模型，这对完成通用计算来说是个非常难用的编程模型

## Slide 58: General-Purpose GPUs (GP-GPUs)
2006年, Nvidia 的 GeForce 8800 GPU 支持一种新的编程语言: CUDA
  “Compute Unified Device Architecture”
  随后工业界推出OpenCL，与CUDA具有相同的ideas, 但独立于供应商
Idea: 针对通用计算，发挥GPU的计算的高性能和存储器的高带宽来加速一些通用计算中的核心（Kernels）
一种附加处理器模型（GPU作为附加设备）：Host CPU发射数据并行的kernels 到GP-GPU上运行
我们仅讨论Nvidia CUDA样式的简化版本，仅考虑GPU的计算核部分，不涉及图形加速部分

## Slide 59: Simplified CUDA Programming Model
计算由大量的相互独立的线程(CUDA threads or microthreads) 完成，这些线程组合成线程块（thread blocks）
// C version of DAXPY loop.
void daxpy(int n, double a, double*x, double*y)
{ for (int i=0; i<n; i++)
y[i] = a*x[i] + y[i]; }
// CUDA version.
__host__ // Piece run on host processor.
int nblocks = (n+255)/256; // 256 CUDA threads/block
daxpy<<<nblocks,256>>>(n,2.0,x,y);
__device__ // Piece run on GP-GPU.
void daxpy(int n, double a, double*x, double*y)
{ int i = blockIdx.x*blockDim.x + threadId.x;
if (i<n) y[i]=a*x[i]+y[i]; }

## Slide 60: Programmer’s View of Execution
blockIdx 0
threadId 0
threadId 1
threadId 255
blockIdx 1
threadId 0
threadId 1
threadId 255
blockIdx
(n+255/256)
threadId 0
threadId 1
threadId 255
创建足够的线程块以适应输入向量
(Nvidia 中将由多个线程块构成的、在GPU上运行的代码 称为Grid，Grid可以是2维的)
Conditional (i<n) turns off unused threads in last block
blockDim = 256 (programmer can choose)

## Slide 61: Hardware Execution Model
GPU
GPU 由多个并行核构成，每个核包含一个多线程SIMD处理器（包含多个车道）
CPU 发送整个 “grid”到GPU，由GPU将这些线程块分发到多个核上（每个线程块在一个核上运行）
  GPU上核的数量对程序员而言是透明的
Core 0
Lane 0
Lane 1
Lane 15
Core 1
Lane 0
Lane 1
Lane 15
Core 15
Lane 0
Lane 1
Lane 15
GPU Memory
CPU
CPU Memory

## Slide 62: Using CPU+GPU Architecture
异构系统（异构多核）
针对每个任务选择合适的处理器和存储器
通用CPU 适合执行一些串行的线程
  串行执行快
  带有cache，访问存储器延时低
GPU 适合执行大量并行的线程
  可扩放的并行执行
  高带宽的并行存取
GPU
SMem
SMem
SMem
PCIe
Bridge
Host Memory
CPU
Cache
Device Memory
Cache

## Slide 63: Threads and Blocks
一个线程对应一个数据元素
大量的线程组织成很多线程块
许多线程块组成一个网格
GPU 由硬件对线程进行管理
  Thread Block Scheduler
  SIMD Thread Scheduler

## Slide 64: CUDA：“Single Instruction, Multiple Thread”
GPUs 使用 SIMT模型, 每个CUDA线程的标量指令流汇聚在一起在硬件上以SIMD方式执行 (Nvidia groups 32 CUDA threads into a warp)
µT0
µT1
µT2
µT3
µT4
µT5
µT6
µT7
ld x
mul a
ld y
add
st y
Scalar instruction stream
SIMD execution across warp

## Slide 65: Thread blocks execute on an SM Thread instructions execute on a core
Registers
GPU
SMs:
SMem
SMem
SMem
PCIe
Bridge
Host Memory
CPU
Cache
Device Memory
Cache
Block
Per-block Shared
Memory
Per-app
Device Global
Memory
Per-thread
Local Memory
Thread
float myVar;
__shared__ float shVar;
__device__ float glVar;

## Slide 66: CUDA kernel maps to Grid of Blocks
kernel_func<<<nblk, nthread>>>(param, … );
GPU
SMs:
SMem
SMem
SMem
PCIe
Bridge
Host Memory
CPU
Cache
Device Memory
Cache
. . .
Host Thread
Grid of Thread Blocks
econve

## Slide 67: NVIDIA Instruction Set Arch.
ISA 是硬件指令集的抽象
  “Parallel Thread Execution (PTX)”
  使用虚拟寄存器
  用软件将其翻译成机器码
  Example:
  shl.s32 R8, blockIdx, 9 ; Thread Block ID * Block size (512 or 29)
  add.s32 R8, R8, threadIdx ; R8 = i = my CUDA thread ID
  ld.global.f64 RD0, [X+R8] ; RD0 = X[i]
  ld.global.f64 RD2, [Y+R8] ; RD2 = Y[i]
  mul.f64 R0D, RD0, RD4 ; Product in RD0 = RD0 * RD4 (scalar a)
  add.f64 R0D, RD0, RD2 ; Sum in RD0 = RD0 + RD2 (Y[i])
  st.global.f64 [Y+R8], RD0 ; Y[i] = sum (X[i]*a + Y[i])

## Slide 68: Conditionals in SIMT model
简单的 if-then-else 编译为谓词（有条件）执行等价于在向量屏蔽寄存器的作用下的向量运算
比较复杂的控制流编译生成分支
如何处理分支？
µT0
µT1
µT2
µT3
µT4
µT5
µT6
µT7
tid=threadid
If (tid >= n) skip
Call func1
add
st y
Scalar instruction stream
SIMD execution across warp
skip:

## Slide 69: Conditional Branching
与向量结构类似, GPU 使用内部的屏蔽字(masks)
还使用了
  分支同步堆栈
    保存分支成功的路径地址
    保存该路径的每个SIMD lane 的屏蔽字(mask)
      即指示哪些车道可以提交结果 (all threads execute)
  指令标记(instruction markers）
    管理何时分支到多个执行路径，何时路径汇合
PTX层
  CUDA线程的控制流由PTX分支指令(branch、call、return and exit）
  由程序员指定的每个线程车道的1-bit谓词寄存器
GPU硬件指令层,控制流包括：
  分支指令(branch,jump call return)
  特殊的指令用于管理分支同步栈
  GPU硬件为每个SIMD thread 提供堆栈保存分支成功的路径
  GPU硬件指令带有控制每个线程车道1-bit谓词寄存器

## Slide 70: Branch divergence
硬件跟踪各µthreads转移的方向（判定哪些是成功的转移，哪些是失败的转移）
如果所有 线程所走的路径相同，那么可以保持这种 SIMD fashion
如果各线程选择的方向不一致，那么创建一个屏蔽（mask） 向量来指示各线程的转移方向（成功、失败）
继续执行分支失败的路径，将分支成功的路径压入硬件堆栈（分支同步堆栈），待后续执行
SIMD 车道何时执行分支同步堆栈中的路径?
  通过执行pop操作，弹出执行路径以及屏蔽字，执行转移成功路径
  SIMD lane完成整个分支路径执行后再执行下一条指令 称为converge(汇聚）

## Slide 71: Example
if (X[i] != 0)
X[i] = X[i] – Y[i];
else X[i] = Z[i];
ld.global.f64 RD0, [X+R8] ; RD0 = X[i]
setp.neq.s32 P1, RD0, #0 ; P1 is predicate register 1
@!P1, bra ELSE1, *Push ; Push old mask, set new mask bits
; if P1 false, go to ELSE1
ld.global.f64 RD2, [Y+R8] ; RD2 = Y[i]
sub.f64 RD0, RD0, RD2 ; Difference in RD0
st.global.f64 [X+R8], RD0 ; X[i] = RD0
@P1, bra ENDIF1, *Comp ; complement mask bits
; if P1 true, go to ENDIF1
ELSE1: ld.global.f64 RD0, [Z+R8] ; RD0 = Z[i]
st.global.f64 [X+R8], RD0 ; X[i] = RD0
ENDIF1: <next instruction>, *Pop ; pop to restore old mask

## Slide 72: Warps are multithreaded on core
一个 warp 由 32个 µthreads 构成
多个warp线程在单个核上交叉运行，以隐藏存储器访问呢和功能部件的延迟
单个线程块包含多个warp (up to 512 µT max in CUDA), 这些warp都映射到同一个核上
多个线程块也可以在同一个核上运行
[Nvidia, 2010]

## Slide 73: SIMT Warp Execution in the SM
Warp: 一组32个CUDA 线程，构成一条SIMD指令
SIMT: Single-Instruction Multi-Thread 建立适用于warp的并行线程的指令
SM 双发射流水线选择两个warp 发射到并行的核上
SIMT warp 执行warp中的指令（SIMD指令）(32个CUDA thread）
通过谓词寄存器控制单个线程(CUDA thread ) 执行结果(enable/disable)
通过同步堆栈管理线程的分支
通过规整的一致的计算来处理分支速度高于非规整的分支转移

## Slide 74: GPU Memory Hierarchy
[ Nvidia, 2010]

## Slide 76: Nvidia Fermi GF100 GPU
[Nvidia, 2010]

## Slide 77: Fermi “Streaming Multiprocessor” Core

## Slide 78: Fermi Dual-Issue Warp Scheduler

## Slide 79: Apple A5X Processor for iPad v3 (2012)
12.90mm x 12.79mm
45nm technology
[Source: Chipworks, 2012]

## Slide 80: Loop-Level Parallelism
研究的焦点问题是：在循环结构中，后面的循环是否依赖于前面的循环
  Loop-carried dependence
Example 1:
for (i=999; i>=0; i=i-1)
x[i] = x[i] + s;
循环级并行：No loop-carried dependence

## Slide 81: Loop-Level Parallelism
Example 2:
for (i=0; i<100; i=i+1) {
A[i+1] = A[i] + C[i]; /* S1 */
B[i+1] = B[i] + A[i+1]; /* S2 */
}
S1 and S2 均使用了前一次循环的结果
S2 使用同一循环中的S1的结果

## Slide 82: Loop-Level Parallelism
Example 3:
for (i=0; i<100; i=i+1) {
A[i] = A[i] + B[i]; /* S1 */
B[i+1] = C[i] + D[i]; /* S2 */
}
S1 使用了S2前一次循环的结果，但数据依赖没有形成环路，也是循环级并行。
Transform to:
A[0] = A[0] + B[0];
for (i=0; i<99; i=i+1) {
B[i+1] = C[i] + D[i];
A[i+1] = A[i+1] + B[i+1];
}
B[100] = C[99] + D[99];

## Slide 83: Loop-Level Parallelism
Example 4:
for (i=0;i<100;i=i+1) {
A[i] = B[i] + C[i];
D[i] = A[i] * E[i];
}
Example 5:
for (i=1;i<100;i=i+1) {
Y[i] = Y[i-1] + Y[i]; //递推关系
}
通常循环间相关表现形式为：递推关系

## Slide 84: Finding dependencies
Assume indices are affine:
  a x i + b (i is loop index)
Assume:
  Store to a x i + b, then
  Load from c x i + d
  i runs from m to n
  Dependence exists if:
    Given j, k such that m ≤ j ≤ n, m ≤ k ≤ n
    Store to a x j + b, load from a x k + d, and a x j + b = c x k + d

## Slide 85: Finding dependencies
通常在编译时无法确定是否相关
数据依赖关系的测试
  GCD test:
    如果存在相关，那么 GCD(c,a) 必须能整除 (d-b)
Example:
  for (i=0; i<100; i=i+1) {
  X[2*i+3] = X[2*i] * 5.0;
  }

## Slide 86: Finding dependencies
Example 2:
  for (i=0; i<100; i=i+1) {
  Y[i] = X[i] / c; /* S1 */
  X[i] = X[i] + c; /* S2 */
  Z[i] = Y[i] + c; /* S3 */
  Y[i] = c - Y[i]; /* S4 */
  }
反相关和输出相关
通过重命名消除这两类相关

## Slide 87: Reductions
Reduction Operation:
for (i=9999; i>=0; i=i-1)
sum = sum + x[i] * y[i];
Transform to…
for (i=9999; i>=0; i=i-1)
sum [i] = x[i] * y[i];
for (i=9999; i>=0; i=i-1)
finalsum = finalsum + sum[i]; //该循环存在循环间相关
Do on p processors:
for (i=999; i>=0; i=i-1)
finalsum[p] = finalsum[p] + sum[i+1000*p];
Note: assumes associativity!

## Slide 88: GPU Future
High-end desktops have separate GPU chip, but trend towards integrating GPU on same die as CPU (already in laptops, tablets and smartphones)
  Advantage is shared memory with CPU, no need to transfer data
  Disadvantage is reduced memory bandwidth compared to dedicated smaller-capacity specialized memory system
    Graphics DRAM (GDDR) versus regular DRAM (DDR3)
Will GP-GPU survive? Or will improvements in CPU DLP make GP-GPU redundant?
  On same die, CPU and GPU should have same memory bandwidth
  GPU might have more FLOPS as needed for graphics anyway

## Slide 89: Acknowledgements
These slides contain material developed and copyright by:
  John Kubiatowicz (UCB)
  Krste Asanovic (UCB)
  David Patterson (UCB)
  Chenxi Zhang (Tongji)
UCB material derived from course CS152、CS252